Table of Contents

### Introduction
This section describes the protocol between the control PC and the thermal control unit.

The protocol is command and response format and has the following attributes.
- Start of packet character
  - ‘#’ for command from a master
  - ‘!’ for a response from a slave
- An address, master is 0, slaves are 1 - n
- Sequence number
  - The sequence number sent by the master will be returned back by the slave in replies, this will allow the master to verify whether the response is for the current command.
- Packet length and CRC to protect against corrupt packets.
- End of packet character
### General message format
Following message attributes are present in all messages.

Byte(s)	Data type	Description / Value(s)
1	uint8_t	Start of packet byte / - ‘#’ for packets from master / - ‘!’ for packets from slave
2	uint8_t	Packet length / – this is the entire length of the packet
3, 4	uint16_t	Address / – 0 for master, 1 – n for slaves
5	uint8_t	Sequence number / - chosen by the master, can be any number / - returned by the slave in command response
6	uint8_t	Message number / - identifies the command, i.e. getStatus, startUp, etc.
7 – N	*	Message body if present required for the command
N + 1	uint16_t	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
N + 3	uint16_t	End of packet byte / - ‘\r’ (0x000D)

### Message definitions
### Get status command

Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x00	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get status response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x10	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x01	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Humidity alert / 0 – no alert present / 1 – alert present – humidity is at or above the threshold
9, 10	uint16_t	0x0000 / or / 0x0001	TECs running / 0 – TECs are not running / 1 – TECs are running
11, 12	uint16_t	0x0000 / or / 0x0001	Chiller running / 0 – chiller is not running / 1 – chiller is running
13, 14	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
15, 16	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Set humidity threshold command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000C	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x02	Message number
7, 8	uint16_t	0x0020	Humidity threshold in network byte order, hex value, for example: / - 0x0020 is 32 – 32% humidity will be the new threshold / - 0x0030 is 48 – 48% humidity will be the new threshold
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Set Humidity threshold response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 12)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x03	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / 0 – fail / 1 – success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get humidity threshold command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x04	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get humidity threshold response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x000C	Packet length (hex value for length 12)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x05	Message number
7, 8	uint16_t	0x0040	Current threshold in network byte order, hex value, for example / - 0x0040 – current threshold is 64% humidity
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get humidity command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x06	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get humidity response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0012	Packet length (hex value for length 18)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x07	Message number
7 - 14	uint8_t	8 byte null term string	Current humidity in null terminated ASCII string, for example client will send: / - “47.9”0x00 for 47.9% humidity / - “58.3”0x00 for 58.3% humidity
15, 16	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
17, 18	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Set TEC set point temperature command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0014	Packet length (hex value for length 20)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x08	Message number
7, 8	uint16_t	0x0002	TEC address to set, 16bit integer value in network byte order
9 - 16	uint8_t	8 byte null term string	TEC temperature in null terminated ASCII string, for example master will send something like the following, leading +/- sign supported, two decimal points supported. / - “-23.71”0x00 for -23.71C for the TEC / - or “5”0x00 for +5.00C for the TEC / - or “+10.83” for +10.83C for the TEC
17, 18	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
19, 20	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Set TEC set point temperature response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x000E	Packet length (hex value for length 14)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x09	Message number
7, 8	uint16_t	0x02	TEC address, hex, network byte order
9, 10	uint16_t	0x0000 / or / 0x0001	Result / 0 – fail / 1 – success
11, 12	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
13, 14	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get TEC set point temperature command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000C	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x0A	Message number
7, 8	uint16_t	0x0002	TEC address, hex, network byte order
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11,12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get TEC set point temperature response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0014	Packet length (hex value for length 20)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x0B	Message number
7, 8	uint16_t	0x0002	TEC address, hex, network byte order
9 - 16	uint8_t	8 byte null term string	TEC temperature in null terminated ASCII string, for example client will send something like the following, leading +/- sign supported, two decimal points supported. / - “-23.71”0x00 for -23.71C for the TEC / - or “5”0x00 for +5.00C for the TEC / - or “+10.83” for +10.83C for the TEC
17, 18	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
19, 20	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get TEC object temperature command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000C	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x0C	Message number
7, 8	uint16_t	0x0002	TEC address, hex, network byte order
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11,12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get TEC object temperature response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0014	Packet length (hex value for length 20)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x0D	Message number
7, 8	uint16_t	0x0002	TEC address, hex, network byte order
9 - 16	uint8_t	8 byte null term string	TEC temperature in null terminated ASCII string, for example client will send something like the following, leading +/- sign supported, two decimal points supported. / - “-23.71”0x00 for -23.71C for the TEC / - or “5”0x00 for +5.00C for the TEC / - or “+10.83” for +10.83C for the TEC
17, 18	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
19, 20	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get TEC information command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000C	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x0E	Message number
7, 8	uint16_t	0x0002	TEC address, hex, network byte order
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11,12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get TEC information command response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0014	Packet length (hex value for length 20)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x0F	Message number
7, 8	uint16_t	0x0002	TEC address, hex, network byte order
9 - 12	uint32_t	0x1234	TEC device type – see Meerstetter documentation
13 - 16	uint32_t	0x1234	h/w version – see Meerstetter documentation
17 - 20	uint32_t	0x1234	f/w version – see Meerstetter documentation
21 – 22	uint16_t	0x00	Pad
23 – 26	uint32_t	0x1234	Serial number – see Meerstetter documentation
27, 28	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
29, 30	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Enable TECs command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x10	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Enable TECs command response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x11	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / - 0x0000 fail / - 0x0001 success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Disable TECs command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x12	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Disable TECs response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x13	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / - 0x0000 fail / - 0x0001 success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Set chiller set point temperature command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0012	Packet length (hex value for length 18)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x14	Message number
7 - 14	uint8_t	8 byte null term string	Chiller set point temperature in null terminated ASCII string, for example master will send something like the following, leading +/- sign supported, two decimal points supported. / - “-23.71”0x00 for -23.71C / - or “5”0x00 for +5.00C / - or “+10.83” for +10.83C
15, 16	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
17, 18	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Set chiller set point temperature response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x000C	Packet length (hex value for length 14)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x15	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / 0 – fail / 1 – success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get chiller set point temperature command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000A	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x16	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get chiller set point temperature response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0012	Packet length (hex value for length 20)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x17	Message number
7 - 14	uint8_t	8 byte null term string	Chiller set point temperature in null terminated ASCII string, for example client will send something like the following, leading +/- sign supported, two decimal points supported. / - “-23.71”0x00 for -23.71C / - or “5”0x00 for +5.00C / - or “+10.83” for +10.83C
15, 16	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
17, 18	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get chiller circulating temperature command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000A	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x18	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get chiller circulating temperature response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0012	Packet length (hex value for length 20)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x19	Message number
7 - 14	uint8_t	8 byte null term string	Chiller set point temperature in null terminated ASCII string, for example client will send something like the following, leading +/- sign supported, two decimal points supported. / - “-23.71”0x00 for -23.71C / - or “5”0x00 for +5.00C / - or “+10.83” for +10.83C
15, 16	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
17, 18	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Start chiller command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x1A	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Start chiller response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x1B	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / - 0x0000 fail / - 0x0001 success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Stop chiller command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x1C	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Stop chiller response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x1D	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / - 0x0000 fail / - 0x0001 success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get chiller information
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x000A	Packet length (hex value for length 12)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x1E	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Get chiller information response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0012	Packet length (hex value for length 20)
3, 4	uint16_t	0x0000	Master address in network byte order
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x1F	Message number
7 - 27	uint8_t	20 byte null term string	Chiller name – see Huber documentation
28, 29	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
30, 31	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Start up command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x20	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Start up response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x21	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / - 0x0000 fail / - 0x0001 success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Shutdown command
Byte	Data type	Value	Description
1	uint8_t	‘#’	Start of packet byte
2	uint8_t	0x0A	Packet length (hex value for length 10)
3, 4	uint16_t	0x0001	Address in network byte order (assuming sending to slave ID 1)
5	uint8_t	0x01	Sequence number (master can pick any number)
6	uint8_t	0x22	Message number
7, 8	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
9, 10	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)

### Shutdown response
Byte	Data type	Value	Description
1	uint8_t	‘!’	Start of packet byte
2	uint8_t	0x0C	Packet length (hex value for length 16)
3, 4	uint16_t	0x0000	Master address
5	uint8_t	0x01	Sequence number (from command)
6	uint8_t	0x23	Message number
7, 8	uint16_t	0x0000 / or / 0x0001	Result / - 0x0000 fail / - 0x0001 success
9, 10	uint16_t	TODO:	CRC / - cyclic redundancy code over the packet not including this CRC and the end of packet byte
11, 12	uint16_t	0x000D	End of packet byte / - ‘\r’ (0x000D)